## Slide 1: PURE PURSUIT Control ALGORITHM

## Slide 2: Introduction
Pure Pursuit Control is a type of Geometric Vehicle model; one of the common path tracking methods used in vehicle tracking.
Exploits the geometric relationship between the course path and the path in which vehicle is heading.
It makes use of look ahead distance to measure the error ahead of the vehicle.

## Slide 3: Geometrical Interpretation
Pure Pursuit algorithm consists of calculating the curvature of circular arc that connects it to the wheel-base to a goal point which is ahead of the vehicle.
The goal point is determined from a look ahead distance ld from the current rear-axle position to the desired path.

## Slide 4
Goal Point (x,y)
Ld- Look Ahead Distance, A parameter of pure pursuit algorithm
Follow the arc to reach the goal point
Do you see problem here?
Y
x

## Slide 5
Goal Point (x,y)
Ld- Look Ahead Distance
But the arc is not unique
How do we make it unique?
x
Y

## Slide 6
Goal Point (x,y)
Ld- Look Ahead Distance
r
Constrain the center of arc to be on Y axis
Y
d
And after simple math we get this equation:-
r = Ld^2/2 Y
Curvature is the inverse of radius.
K = 2Y/Ld^2, K = curvature.
Steering angle should be proportional to the curvature of the arc.
x
Y

## Slide 7: Now that we know how to find arc to a given wave-point, how do we pick up current wave-point from the list of wave points?
Pick the wave-point that is closest to the vehicle.
Go up to the wave-point that is one look-ahead distance away from the vehicle.
Use that as the current wave-point.
If there are no wave-points exactly one look-ahead distance away from the car, then choose the next best one.

## Slide 8: How to Update the goal point?
Each time we find the current position of the car:
  Find the current wave-point
  Actuate the steering angle towards that wave-point
  Localize to find the new position
  Repeat.

## Slide 9: THANKYOU
A short summary which encapsulates an introduction and how the algorithm works.